## Slide 1: PC615 Meteor/Arrow Lake OPS WITH MOBILE CPU
Plug-in Module
System | 
System Memory | Up to 96GB, 2 x SO-DIMM DDR5-5600 MHz
Storage | 1 x M.2 (2242/2280)PCIE4.0 x4 & SATA SSD; 1 x M.2 (2280)PCIE4.0 x1 for SSD
TPM | Optional: TPM2.0
Watchdog Timer | Yes
Auto Power On | Yes
RTC | Set up independently every day, a week as a cycle
Remo on | NA
Power Requirement | DC jack/80pin JAE DC-IN, 12 V~19 V
Dimensions | 200 mm x 119 mm x 30 mm (7.87” x 4.69” x 1.18”)
Construction | Metal, Black
Operating System | Windows 11 (64bit) /Linux Ubuntu (64bit)
Operating Temperature | 0°C ~45°C (32°F~113°F) @0.7m/s Air Flow
Humidity | 95% @ 45°C (non-condensing)
Certifications | CE, FCC Class B
JAE support HDMI/DP output 1 x DP (5120 x 2880 @60 Hz)
Support Wi-Fi/BT module
Intel® Core™ Ultra Series 1/2processors
Optional Intel® vPro® technology
CPU | 
CPU | Intel® CoreTM U5-125U processor Intel® CoreTM U7-155U processor Intel® CoreTM U5-125H processor Intel® CoreTM U7-155H processor
Chipset | SoC
Total Cores | 12 Cores / 10 Cores / 10 Cores
Total Threads | 8 / 14 / 16
TDP | 15 W/28 W
Display | 
GPU | Intel® Arc™ graphics
Graphic Engine | DirectX12.1, OpenGL4.6, OpenCL3.0 Intel® Quick Sync Video
Display Interface | 1 x HDMI (Max.4096 x 2160 @60 Hz) 1 x DP (Max.4096 x 2160 @60 Hz)
JAE Interface | DP/HDMI (Max. 5120 x 2880 @60Hz)
I/O interface | 
USB | x USB Type-C3.2 Gen1, x USB3.2 Gen1, 2 x USB2.0
Serial Port | NA
Audio | 1 x MIC-IN, 1 x AUDIO-OUT
Button | 1 x Power on, 1 x CLR-CMOS
Antenna | 2 x Connector for Wi-Fi/BT
Network | 
Network Controller | 1 x Intel® i219LM Gigabit Ethernet
Ethernet Interface | 1 x RJ45
Wi-Fi/BT | 1 x E-Key M.2 (2230) for Wi-Fi/BT Support Wi-Fi 6E, Wi-Fi 7 (CNVi)
Mobile Network | NA

## Slide 2
www.giadatech.com
Dimensions and Drawing
All product specifications are subject to change without notice
The terms HDMl, HDMl High-Definition Multimedia Interface, and the HDMl Logo are trademarks or registered trademarks of HDMl Licensing Administrator, Inc.
Optional items | 
Wi-Fi/BT Module | Wi-Fi 6E (802.11ax): Intel® Wi-Fi 6E AX210 Wi-Fi 7 (802.11be): Intel® Wi-Fi 7 BE201
Operating System License | Windows 11 (64bit)
Order information | 
PC615-125U40N0G-GIA | CPU: Intel® CoreTM iU5-125U
PC615-155U40N0G-GIA | CPU: Intel® CoreTM iU7-155U
PC615-125H40N0G-GIA | CPU: Intel® CoreTM U5-125H
PC615-155H40N0G-GIA | CPU: Intel® CoreTM U5-155H
Packing List | 2 x Wi-Fi Antenna
Package | Carton, EPE